## Slide 1: FOTA
FIRMWARE OVER THE AIR

## Slide 2: FOTA SYSTEM DEFINITION
Firmware Over-The-Air, or "FOTA", is a way in which the firmware of a device is updated wirelessly by the manufacturer. Firmware runs in the background and is there to make sure the device's hardware runs properly.

## Slide 3: TABLE OF CONTENTS 01 02 03 04
Introduction
Problem Statement
Objective & Goals
System Overview

## Slide 4: TABLE OF CONTENTS 06 07
Bootloader
05
FOTA System
System Flow and Hardware Design
Automotive Cybersecurity Techniques
08
Mobile Application

## Slide 5: TABLE OF CONTENTS 09
FOTA
Server
10
Testing and Validation

## Slide 6: — Nikola Tesla
“When wireless is perfectly applied the whole earth will be converted into a huge brain.”

## Slide 7: INTRODUCTION 01

## Slide 8: INTRODUCTION
In today's world, most devices have at least 100 million lines of code. So, when a company wants to add a new feature to a device, it's not practical to do it manually. Instead, they use automated methods.
Since the 1960s, cars have gone from being mostly mechanical to incorporating a lot of software, making them what we now call “SDV (Software Defined Vehicles)." This shift represents a big change in how cars work.

## Slide 9: PROBLEM STATEMENT 02

## Slide 10: PROBLEM STATEMENT
  In today's technology-driven world, Smart Cars are equipped
  with complex coding that requires regular updates to enhance
  features and fix bugs. The manual updating of each car at the
  Original Equipment Manufacturer (OEM) level would be a
  highly impractical task.
  Impleme­nting this approach could potentially lead to customer dissatisfaction, especially in cases where crucial bugs need urgent attention but cannot be promptly resolved. He­nce, there is an urge­nt requirement for an automate­d system that can streamline the­ process of updating and fixing bugs efficiently.

## Slide 11: A PICTURE IS WORTH A THOUSAND WORDS

## Slide 12: Ford Recalls More Than 430,000 Vehicles Due to Software Defects
- The Guardian

## Slide 13: OBJECTIVES & GOALS 03

## Slide 14: OBJECTIVES & GOALS
Time-Saving
Bug Fixing
Cost-Effective
More Secure

## Slide 15: SYSTEM OVERVIEW 04

## Slide 16: SYSTEM OVERVIEW
SERVER
VEHICLE
ORIGINAL EQUIPMENT MANUFACTURER (OEM)
01
02
03
Uploading
Update
WIFI Channel

## Slide 17: FOTA SYSTEM 05
System Flow and Hardware Design

## Slide 18
FOTA refers to the technology that allows manufacturers to wirelessly update the firmware of electronic control units (ECUs) in vehicles. This capability enables the delivery of new features, bug fixes, and performance improvements without requiring physical access to the vehicle.
With increased connectivity, vehicles are more vulnerable to cyberattacks. Ensuring the security of automotive systems is critical to protect against unauthorized access, data breaches, and potential physical harm.
FOTA OVERVIEW

## Slide 19: HARDWARE DESIGN
OEM Server
User Interface
Requests
Electronic Control Unit
STM32F401RCT6 (Black Pill)
Obstacles Avoidance
Car
Gateway
NodeMCU ESP32
Bluetooth Module
HC-05
Application

## Slide 20: Dual-function ECU
The STM32F401RCT6 is utilized as a Two-View Electronic Control Unit (ECU), functioning both as the Main ECU and the Application ECU.
Electronic Control Unit
STM32F401RCT6 (Black Pill)
Main ECU: flashing of code and the OTA updates via the bootloader.
Application ECU: integrating peripherals with the hardware components to work with the Obstacles Avoidance Vehicle.
Linker script file is essential in configuring the STM32F401RCT6 (Black Pill) to operate as a dual-function Electronic Control Unit (ECU).

## Slide 21: Memory Architecture
Main Memory Consists of
12 Sectors.
The Bootloader Starts From
Sector 0 to Sector 2.
The Application Starts From
Sector 2 at address 0x8008000.

## Slide 22: Application ECU
The Application is responsible for managing the car's behavior, focusing on obstacle detection and avoidance.
It interfaces with DC motors, ultrasonic sensor to navigate the car safely and a buzzer to alert obstacle detection.
This entire process operates in a feedback loop, continuously detecting obstacles, measuring distances, and adjusting motor controls to dynamically navigate the vehicle around obstacles and avoid it efficiently.

## Slide 23: SYSTEM FLOW
Vehicle Owner
OEM
Target Memory Sector
User Interface
Wireless Media
OEM Server
Critical update
Additional feature
Update Begins
Accepted
Update
Snoozed
Releases new firmware update
Reports problem
Refused
Gateway
Firmware update
Flashing Firmware
Bootloader
Request
Response

## Slide 24: Bootloader 06

## Slide 25: Bootloader
Bootloader is a small program that resides in the non-volatile memory of a microcontroller. Its primary function is to initialize the system and load the main application program (firmware) into the system’s flash memory for execution.
The bootloader’s most critical function is to load the main application firmware into memory.

## Slide 26: Bootloader Commands Handling
Sector Erase of the User flash
Slide By: Eng. Ahmed Abd El-Ghafar

## Slide 27: Bootloader Commands Handling
Write data into different memories of the MCU
Slide By: Eng. Ahmed Abd El-Ghafar

## Slide 28: Bootloader Commands Handling
Jump Bootloader to specified address
Slide By: Eng. Ahmed Abd El-Ghafar

## Slide 29: Automotive Cybersecurity Techniques 07

## Slide 30: Automotive Cybersecurity Techniques

## Slide 31: Automotive Cybersecurity Techniques
In today's digital age, data security is crucial. With increased reliance on online platforms, the risks of breaches and cyberattacks rise. Ensuring data confidentiality, integrity, and availability is essential for compliance and trust.
In addition to encryption, we have also conducted extensive penetration testing on our servers. Penetration testing involves simulating cyberattacks on our systems to identify and address potential vulnerabilities before they can be exploited by real attackers.
Firstly, we have implemented a robust encryption algorithm. This ensures that all data transmitted within our network is rendered unreadable to unauthorized parties, effectively protecting it from interception and eavesdropping attempts by malicious actors. Encryption serves as the first line of defence.

## Slide 32: Encryption
We use the AES encryption algorithm to secure our data. AES, or Advanced Encryption Standard, is a highly secure and widely trusted method for protecting information from unauthorized access.
We used AES-128 encryption algorithm

## Slide 33: Securing Server
Admin
Login (2FA)
OEM Server
Upload Firmware
Client
Members

## Slide 34: Mobile Application 08

## Slide 35: Mobile Application
The Mobile Application is designed to run on the dashboard within the vehicle, simplifying the user's interaction with the system and providing a responsive dashboard for the vehicle.
User interacts with simple UI and choose from different buttons on the Mobile Application.

## Slide 36: Wireless Connection
Purpose:
Functionalities:
Enables the app to send and receive data wirelessly.
Facilitates functionalities like vehicle control, Report a Problem and Notifications.
Establishes a connection between the app and vehicle via the HC-05 Bluetooth module.
Establishes a connection between the app and Server via the Wi-Fi Connection.

## Slide 37: Functionalities: Report A Problem
This is an essential feature that allows the user to report any issues they are having with the system to the server.
The technical team will then attempt to resolve the issue and notify the user of any updates.

## Slide 38: Functionalities: Service Stations
If the user encounters any problems in the car that cannot be solved using Software Updates, he can use this option to search for the nearby service stations to him and go to them directly.
This functionality depended on the device's built-in location services through Google Maps APIs.
Greater compatibility across different devices.
Reduced hardware costs.
Simplified maintenance.
Allows for more frequent updates and improvements.
Benefits of shifting from a GPS hardware module to a software solution:

## Slide 39: Functionalities: Vehicle Control
Purpose: Controls vehicle movement in four directions: forward, backward, left, and right.
Operation:
Users press buttons to send movement commands to the vehicle.
In real life we don’t need this functionality as it’s used only to test the vehicle movements.
Commands are executed remotely using the Bluetooth module.

## Slide 40: Notification and Alerts
Notifications and alerts are one of the most important means of communication between the user and the server, as the application always listens to the server and waits until there is an update.
There are two types of notifications:
Critical update notifications: when the update is mandatory and no choice to snooze it.
Additional Feature Update notifications: when the update is optional, and the user can accept or snooze it.

## Slide 41: FOTA SERVER 09

## Slide 42: Organization and Privileges
Organization:
Admins: System Managers, Extensive Capabilities.
Users: Task-Specific Operators, Limited Access.
Privileges:
Admins: Add/Delete Users , Change Roles, Update Credentials, Manage Files and Tickets.
Users: Upload/Download Files, Send Updates to Clients, Receive Tickets.

## Slide 43: Server Workflow: User
Login Process:
  Standard Login: Users enter credentials → Enter OTP.
  First-Time Login: Users enter credentials → QR code pops up → Scan QR code with Google Authenticator → Enter OTP.
  Forgot QR Code: Users can request a new QR code from admins.
File Management:
  Upload Files: Users can upload files to the server.
  Update Types:
    Critical Update: Push updates to clients.
    Feature Addition: Pull updates.

## Slide 44: Server Workflow: User
Client Ticket Management:
    View and Handle Tickets:
      Users can view tickets from clients.
      Handle client tickets during subsequent updates.

## Slide 45
Login Process:
  Standard Login: Admins enter credentials → Enter OTP.
Support Actions:
  Resend QR Code: Admins can resend QR codes to users if forgotten.
  Admin QR Code: Admins can retrieve their QR code if forgotten.
Server Workflow: Admin

## Slide 46: Access Control
Personal Dashboard:
  Individualized dashboard for each user
  File Visibility: Only user-uploaded files are visible.
  Ticket Visibility: All client tickets are visible to users.
File Access Control:
  Tracking: Includes upload time, uploader’s identity, and file name.
  Audit Trail: Facilitates issue tracking.
  Activity Logs: Logs for each admin's recent actions.
  Admin Panel Actions: Includes admin panel activities.
Admin Access Control

## Slide 47: Security Features
Two-Factor Authentication (2FA):
  TOTP (Time-based One Time Password) for enhanced user authentication.
Data Encryption:
  AES encryption for database file storage.
Password Security:
  Passwords hashed in the database using sha256(pbkdf2) algorithm.
Penetration Testing:
Regular tests to identify and fix vulnerabilities, including prevention of injection attacks, secure handling of file upload, and access broken control.

## Slide 48: Testing and Validation 10

## Slide 49: V MODEL

## Slide 50: V MODEL STAGES

## Slide 51: SYSTEM FLOW

## Slide 52: THANKS!